## Slide 1
PLANING ANALYSIS AND DESIGN OF G+3
RESIDENTIAL BUILDING WITH EVAPOTRANSPIRATION BASIN
GUIDED BY Mr. P. SRI BALAJI (ASSISTANT PROFESSOR)
NAVEEN. C 312318103034
Batch 11

## Slide 2: ABSTRACT
In this project we have planned, analyzed and designed a G+3
Residential building. For this Requirement a G+3 residential
Building is planned using the popular drafting software AUTO
CAD 2D. It is further analyzed using the premier analysis
software STADD PRO. Then by using REVIT the 3D view
Of the building is obtained based on the analysis of STADD PRO
The salient features of the G+3 residential building is manually
Designed the design and detailed drawing are represented in
This project work.

## Slide 3
OBJECTIVE :
To make a complete design of the main structural
elements of a residential building with the
sustainable bio tank which including slabs, beams,
and columns. Then these arrangements should
ensure a robust and stable structure which could
not collapse under any effects of accidental damage
to any of these elements.
The design is based on sustainable ideas.

## Slide 4
METHODOLOGY
Plan Preparation or Schedules of drawings
Design / Development
Analysis and Optimizations
Final check out and Report making
Conclusion

## Slide 5: PROJECT DETAILS
Building area : 24x13.21m
Area location : Coimbatore , Tamil Nadu
Purpose of building : RESIDENTIAL BUILDING
No of stories : G+3
Height of each story : 3 m
- Shape of the building : Rectangular
- Grade of concrete : M25
- Grade of steel : Fe 415

## Slide 6: AUTO CADD DRAWING

## Slide 7: AUTO CADD DRAWING

## Slide 8: STRUCTURAL AND CENTRE LINE PLAN DRAWING

## Slide 9: COLUMN LAYOUT

## Slide 10: BEAM LAYOUT

## Slide 11: SLAB LAYOUT

## Slide 12: EVAPTRANSPIRATION BASIN

## Slide 13
3D MODELLING
FRONT VIEW

## Slide 14: ANALYSIS RESULTS 3-D VIEW

## Slide 15: BENDING MOMENT DIAGRAM

## Slide 16: APPLIED DEAD LOADS

## Slide 17: APLLIED LIVE LOADS

## Slide 18: Design of Two Way Slab
SLAB NUMBER : 120
Size of slab = 6.59m X 5.18m
Effective depth, d = 200mm
Overall depth, D = 220mm
Factored load, Wu = 29.625kN/m
Moment, Mux = 73.40kNm
Moment, Muy = 76.366 kNm
Ast=1171mm2 along x direction [Mu = 0.87 fyAst d [1-((Astfy)/(fck b d))]
Reinforcement details
-Along shorter span (x-direction), reinforcement provided is of 16mm bar at 200mm
Ast= 1120.6mm2 along y direction [Mu = 0.87 fyAst d [1-((Astfy)/(fck b d))]
-Along longer span (y-direction), reinforcement provided is of 16mm
bar at200 mm

## Slide 19: REINFORCEMENT OF SLAB

## Slide 20: ANALYSIS RESULTS
CRITICAL BEAM
BEAM NO: 174

## Slide 21: From STADD PRO

## Slide 22: DESIGN OF BEAM
Size of Beam = 350mm X 400mm
Effective span = 6590mm
Effective depth, d = 370mm
Factored moment, Mu(-) = 181.56kNm
Factored moment, Mu(+) = 103.19kNm
MU limit = 193 kN/m (MU limit = 0.138 fck*bd2)
MU< Mu limit
The beam has to be designed for singly reinforced beam
Ast= 1751mm2 [Mu = 0.87 fyAst d [1-((Astfy)/(fck b d))]
Negative reinforcement
-Provide 6nos of 20 mm dia at the top tension face near supports.
Ast= 868.1mm2 [Mu = 0.87 fyAst d [1-((Astfy)/(fck b d))]
Positive reinforcement at midspan
-provide 4 nos of 20 mm dia at bottom tension at center span section

## Slide 23: REINFORCEMENT OF BEAM

## Slide 24: VALUE FROM STADD PRO

## Slide 25: DESIGN OF COLUMN SUBJECTED TO UNIAXIAL BENDING
Size of column = 300mm X 500mm
Effective span =3000mm
Effective length, L eff =2100mm
Factored load, Pu = 2154kN
Factored moment, MUX=108.21kNm
MUY=59.13kNm
Equivalent moment = 1.15 √(Mux2 + Muy2) =141.8kNm
Longitudinal reinforcement
-Provide 10 nos of 20mm bar which is equally distributed on two Sides
Ast provided =3000mm2 (Puz = 0.45fck*Asc+0.75fyAsc )
Lateral ties
-provide 8 dia bar of lateral ties at 250 mm spacing

## Slide 26: REINFORCEMENT OF COLUMN

## Slide 27: CEITICAL COLUMN BI AXIAL

## Slide 29: DESIGN OF COLUMN SUBJECTED TO BIAXIAL BENDING
Size of column = 300mm X 500mm
Effective span = 3000mm
Effective length, El = 2100mm
Factored load, Pu = 1060 kN
Factored Moment , MUX = 133kNm
MUY = 75.5 kNm
Equivalent moment = 1.15 √(Mux2 + Muy2) = 175.5kNm
Longitudinal reinforcement
-Provide 8 nos of 20mm bar which is equally distributed on two sides
Ast provided = 2512mm2 (Puz = 0.45fck xAsc+0.75fyAsc )
Lateral ties
-provide 8 dia bar of lateral ties at 250 mm spacing

## Slide 30: REINFORCEMENT OF COLUMN

## Slide 31: DESIGN OF STAIR CASE
Size of staircase = 2.1*4.5 m
Rise = 150mm
Thread = 280mm
No of flight = 2
Width of the flights = 950mm
Width of the landing = 2050mm
Effective depth = 230mm
Overall depth = 250mm
Total load on Landing = 9 kN/m
Total load on waist portion = 12.125kN/m
MU = 45 kNm ,(MU = 0.138fckbd2)
Ast =575mm2 [Mu = 0.87 fyAst d [1-((Astfy)/(fck b d))]
Main Reinforcement
-Use 12mm dia bar req for each flight @ 200mm spacing
Distribution Reinforcement, Ast= 276mm2
-Use 8 mm dia bar @ spacing 180mm

## Slide 32: REINFORCEMENT OF STAIR CASE

## Slide 33: DESIGN OF FOOTING
Size of footing = 2.48 *1.55m
Overall depth,D = 600mm
Effective depth,d = 550mm
Main Reinforcement
Along xx, Ast =1011.17mm2 [Mu = 0.87 fyAst d [1-((Astfy)/(fck b d))]
-Provide 8 nos of 16 mm dia bar which is equally distributed
Along yy, Ast = 1617.8 mm2 [Mu = 0.87 fyAst d [1-((Astfy)/(fck b d))]
-Provide 5 nos of 16 mm dia bar which is equally distributed
Check for shear τc= 0.92N/mm2, τv =0.33N/mm2
τv<τc
Check for two way shear, τc =1.25N/mm2, τv =0.56N/mm2
τv<τc

## Slide 34: REINFORCEMENT OF FOOTING

## Slide 35: SEPTIC TANK

## Slide 36: DESIGN OF SEPTIC TANK
No of users : 50
Tank size : 4*2.5*2
Overall depth = 230 mm
Effective depth = 200
Factored Load = 11kN/m
Ast =1232.41mm2 (wall), Ast = 395mm2 (roof slab) [Mu = 0.87 fyAst d [1-((Astfy)/(fck b d))]
Main reinforcement for base slab , roof slab ,near face and away face water
-Provide 12 mm bars @ 120 mm c/c
Distribution bars for base slab , roof slab ,near face and away face water
-Provide 10 mm bars @ 120 mm c/c

## Slide 37: REINFORCEMENT OF SEPTIC TANK

## Slide 38: CONCLUSION
Thus the structure has been planned using AUTOCADD software . It has been
Analyzed using STADD PRO. This project Gives us practical knowledge about
How to design a building and its elements as per code book.

## Slide 39: Referred Indian standard codes:
IS-456, Plain and reinforced Concrete-Code of Practice, Bureau of Indian Standards, New Delhi,2000.
IS 875, Code of Practice for Design Loads (Other than Earthquake) for Buildings and Structures- Part 2Imposed Loads, (Second Revision), Bureau of Indian Standards, New Delhi,1987.
SP 16 - 1980 ,Design Aids for Reinforced Concrete to IS:456 - 1978 , Bureau of Indian Standard
New Delhi

## Slide 40: PDF have attached

## Slide 41: THANK YOU